NBR4

Thermal Printer

Instructions

（Ver 1.00）

# Introduction

NPR4 printer is a new line thermal printer, it features in fast speed, low noise, high reliability, perfect quality and ribbon needless, avoiding the vexation of regular maintenance.

NPR4/NPR5 printer is small in outline dimension, simple with operation, and extensive with application, it is especially suitable for commercial cash register, PC-POS, POS bank and all kinds of related industries.

# Chapter 1 Feature and Performance

1.1 Print Performance

● Print method: direct thermal

● Print paper width: 79.5±0.5mm

● Print density: 8 dots/mm, 576 dots/line

● Print speed: approx.250mm／sec.

● Reliability

(1)Print head life: 150km

Using condition:

＊Print 12 × 24 ASCII characters, print 50 lines each time, intermittent print repeatedly

＊Each dot-line printing at the same time should not exceed 25%, each character line and one dot vertical printing repeatedly should not exceed 11 times

＊Use specified thermal paper

（2）Cutter life: 1,000,000 cuts

Using condition: less than 30 cuts/minute

● Valid print width: 72mm

## 1.2 Print Paper

● Thermal paper roll model: TF50KS－E（Japan paper co.ltd）

AF50KS-E (JUJO THERMAL)

● Thermal paper roll: Width－－－ 79.5±0.5mm

Outer Diameter －－－	80mm（max.）

Inner Diameter－－－	 13mm（min.）

Thickness	－－－ 0.06mm～0.08mm

## 1.3 Print Font

● ANK Character Set

12×24 dots，1.5（W）×3.00（H）mm

● GB GB2312-80(Chinese):

24×24 dots，3.00（W）×3.00（H）mm.

## 1.4 Interface

●Internet interface

● USB Interface：

## 1.5 Print Control Commands

●commands Character print: support double-width, double height prints of ANK characters, user-defined characters and Chinese characters, the character line spacing is adjustable.

● Graphics print commands: support the print of bit-map graphics and download bit-map graphics with different density

● GS bar code print command: support UPC-A，UPC-E，EAN-13，EAN-8，CODE39，ITF，CODEBAR，CODE93，CODE128,PDF417,QR bar code print.

## 1.6 Power Supply

● DC24V±10％，2A，A-1009-3P power socket.

## 1.7 Operation Environment

● Operation temperature: 5～50℃; Relative humidity: 10～80％

● Storage temperature: -40～55℃; Relative humidity: 10～90℃

## 1.8 Outline Dimension

●182（L）mm×132（W）mm×133（H）mm

## 1.9 Type

| type | Interface |
| --- | --- |
| NPR4 | USB |

# Chapter 2 Operation Specification

## 2.1 Printer Appearance

## 2.2 Paper Installation

### 2.2.1 Paper Loading

### NPR4/NPR5 adopts thermal paper roll with width of 79.5mm.

Steps of Loading Thermal Paper are as below:

Press the upper cover button on the left side, open the movable upper cover, put paper into the printer and draw the side of the paper roll, put the paper endings on the print head, close the upper cover and press it downwards lightly.

1.Pay attention to the direction of loading paper, make the printing surface face to the print head. 2.Please don’t feed or draw the paper forwards or backwards with hands. 3.Keep clean of the print head, avoid to influence the printing quality.

### 2.2.2 Solution to Paper Jam

If cutter is jammed, turn off the power and turn it on after a while, the cutter will be OK. If paper is jammed, open the paper cover, and take out the paper. If the cutter cannot be OK, open the cover, and turn the white plastic gear by hand to make the cutter be OK.

If cutter is jammed and you do not want to lose the data, you should open the cover without turning off the power and pull the paper out. Printer will have recovered by itself.

## 2.3 Self-test

The Self-test procedure can test the work condition of printer. If the printer can print the self-checking spline, it means the printer can work.                                                           The content of self-test spline should be 96 ANK characters, default code page, name of Chinese Character library, interface setting and software.                                                              Method for self-test: press【FEED】button and turn on the power，   The result is as following:

## 2.4 Hexadecimal Printing

Turn on the printer according to the step below, it will enter the mode of Hexadecimal Printing

1.Open the paper cover.

2.Press【FEED】button，and connect with the power.

3.Close the cover, the printer will print out 3 lines as below:

Hexadecimal Dump

To terminate hexadecimal dump,

## 2.4 Entering upgrading mode

When printer is not connected with power, open the paper cover, press on the 【FEED】 button, then turn on the printer, ERROR light flashes four, release the 【FEED】 button, then press 【FEED】 button four times, then turn on the paper cover, now printer is under upgrading mode and two status lights will alternating flash.

# Text boxes

Warning

This is a class A product. In a domestic environment this product may cause radio interference in which case the user may be

required to take adequate measures.

！Caution!